## Slide 1
2022/3/13
UWB初步调研
汇报人：赵鹏

## Slide 2
2
01
Device

## Slide 3
3
02
Brief Introduction
抗多径能力强
穿透能力较强（宽频谱）
定位精度高（厘米级）
能效高
抗干扰（占空比极小0.01~0.001）
Ultra-Wideband，利用纳秒(ns)至皮秒(ps)级的非正弦波窄脉冲传输数据进行通信

## Slide 4
4
02
Brief Introduction
iphone11就开始引入uwb，三星galaxy note 20 ultra，小米mix4等陆续引入
小米uwb一指连（指向任意智能设备都可直接控制，角度测量精度可达±3°）
在手机查找app中显示大概位置，走到近场后，利用UWB进行精准查找。
通过Siri或者手机界面中的按钮操作，让AirTag发声，从而快速发现设备。
通过NFC贴近AirTag，可以看到联系人信息，相当于电子工牌。

## Slide 5
5
03
vital signals
IQ upconversion and downconversion
carrier frequency is 7.3GHz,
and bandwidth is 1.4GHz

## Slide 6
6
03
vital signals
Fast time: time delay of range distance
Slow time: estimate Doppler effect by observing over a long time span
Basic measurement setup example：
frame length: 50ns (最远
Duration of frame: 0.1s (数量级相差
Pulse Repetition Interval (PRI)
Impulse response

## Slide 7
7
03
vital signals
an example of real received signals from UWB radio
Received baseband signals

## Slide 8
8
03
vital signals
Window size is set to
: estimated by averaging the values around the fast-time index under test
compare value of the fast-time bin under test with ( is empirically set to 1.5)

## Slide 9
9
04
Other Application
核心定位原理：ToA(Time of Arrival)
Examples (from Decawave)
TDoA:
Time Difference of Arrival
TWR:
Two-Way Ranging
PDoA:
Phase Difference of Arrival

## Slide 10
10
04
Other Application
It analyzes the reflected signals to synthesize an image and also to identify the material status.
Embing a rebar into a concrete wall at a depth of 5cm and swipe these devices over the wall surface
SIWA
device

## Slide 11
11
Thanks